## Slide 1: Subject Name : COMPUTER ARCHITECTURE Presentation Title: SOLID STATE DRIVES
Team Members:
Students Name Reg.No:
1.BALAJI R 210618104007
2.PRANESH S 210618104034
3.PARVEEN KUMAR K K 210618104035
4.CHANDRU 210618104010
5.HARIKRISHNAN 210618104018
6.GOKUL 210618104014
JEPPIAAR INSTITUTE OF TECHNOLOGY
“Self-Belief | Self Discipline | Self Respect”
Department of Computer Science and Engineering

## Slide 2: Solid State Drive(SSD)
SSD is an PC storage device that uses Solid State memory to store information.
SSD uses non volatile NAND Flash Memory , which enables it to retain data when the power is removed.

## Slide 3: NAND Flash Memory
NAND Flash Memory is the key component of SSD.
It is a specific type of EEPROM chip.
It has a grid of columns and rows with a cell that has two transistors at each intersection as Control gate and Floating gate transistor.
The principle of operation is based on MOSFETs.

## Slide 4: Types of NAND Flash
Single Level Cell (SLC)
Multi Level Cell (MLC)

## Slide 5: SSD Elements
SSD consists of basically three elements:
SSD Controller.
SSD Flash.
SSD Interface.

## Slide 6: SSD Controller Block Diagram
Processor
ECC
Flash Controller
DRAM Controller
I/O Interface
Controller Memory
Chip Configuration

## Slide 7: SSD Flash Block Diagram
Data Interface
I/O Controller
Control Logic
Address Register
Data/Cache register
Status register
Row/Column Decode
Flash Array

## Slide 8: SSD Interface
Interface is used to connect the SSD with the computer.
Also, since SDDs are generally used in conjunction with magnetic disk drives, a common mass storage bus interface is used in most cases.
SSD are available with a variety of system interfaces based primarily on the performance requirements:
Serial ATA
Serial attached SCSI Fiber Channel
USB

## Slide 9: SSD Storage Scheme
Groups of NAND flash cells are organized into pages and these pages are organized into blocks.
Read and write operations can be performed on pages, but erase operations can only be performed at the block level.
This means that when rewriting a page, the entire block must be erased first.
The SSD controller manages this process.

## Slide 11: SSD Architecture

## Slide 12: SSD Around Us
Mobile Media Players
Solid-State Disks (SSD)
Thumb Disks
Multimedia Memory Cards
Embedded Systems

## Slide 13: Benefits of SSD
Faster start up of Solid State Drive
Faster access
Faster application launch time
More energy efficient
More reliable
More robust under extreme conditions
Lighter

## Slide 14: Application
SSDs were mainly used in those aspects
of mission critical applications where the speed of the storage system needed to be as fast as possible.
Organizations that can benefit from faster access of system data include equity trading companies, telecommunication corporations, and video streaming.
SSD are used as cache at server side of Enterprises.

## Slide 15: Thank You